CREATING RAID 10(1+0) IN CENTOS 7

        FIRST APPROACH

Setting up RAID 10(1+0) in Virtual Machine :

Requirements:
→ Virtual Machine
→ Four disk(minimum)
→ internet connection
→ a static ip address (in case you want to ssh the server)

STEP 1:
Adding four 20GB disk in the centos7 Virtual machine.

STEP2:
Boot the machine.

STEP3:
open Terminal .(or you just ssh the server from the server) [in this case I ssh to the server]

STEP4:
apply the ‘lsblk’ command to see the block devices

=>lsblk

There are three additional block devices name ‘sdb’ and ‘sdc’ and ‘sdd’ we use this three drive to make a raid 5.

STEP5:
install the mdadm package

=>yum update
=> yum install mdadm -y

STEP6:
check the version in the of the packages
=> mdadm –version

STEP7:
Examine the hard drive with mdadm

=> mdadm –examine /dev/sd[b-e]

STEP8:

Create partition for RAID

=>fdisk /dev/sdb

Follow below instructions for creating partitions.
1. Press ‘n‘ for creating new partition.
2. Then choose ‘P‘ for Primary partition.
3. Next select the partition number as 1.
4. Give the default value by just pressing two times Enter key.
5. Next press ‘P‘ to print the defined partition.

Follow below instructions for creating Linux raid auto on partitions.
1. Press ‘L‘ to list all available types.
2. Type ‘t‘to choose the partitions.
3. Choose ‘fd‘ for Linux raid auto and press Enter to apply.
4. Then again use ‘P‘ to print the changes what we have made.
5. Use ‘w‘ to write the changes.

[creating partition]

[creating raid on that partition ]

[see the block devices]

STEP9:

Do the step 8 for the ‘sdc’ ,‘sdd’,’sde’

=>fdisk /dev/sdc
=>fdisk /dev/sdd
=>fdisk /dev/sde

STEP10:

Examine with the ‘lsblk’

=>lsblk

STEP11:

Examine with the ‘mdadm’
=>mdadm –examine /dev/sd[b-e]1

STEP12:

Create RAID md Devices (with miror)

=>mdadm --create /dev/md0 --level=10 --raid-devices=4 /dev/sd[b-e]1

STEP13:

See the Details of the RAID 0 devices

=>mdadm –detail /dev/md0

STEP14:

Varify with this command

=>mdadm -E /dev/sd[b-d]1 | grep raid5

STEP15:

Assigning File partition on the File system

=>mkfs.ext4 /dev/md0

STEP15:

mount the volume
=>mkdir /mnt/raid10
=>mount /dev/md0 /mnt/raid10

STEP16:

check the mounted volume

=>df -h

STEP17:
check the block devices with lsblk

=>lsblk