CREATING RAID 0 IN CENTOS 7

RAID 0 is not fault tolerant but it has some advantage

→ it is high performance
→ no space will be wasted
→ reading and writing speed will be Fast

Setting up RAID 0 in Virtual Machine :

Requirements:
→ Virtual Machine
→ Two disk
→ internet connection
→ a static ip address (in case you want to ssh the server)

STEP 1:
Adding two 20GB disk in the centos7 Virtual machine.

STEP2:
Boot the machine.

STEP3:
open Terminal .(or you jusr ssh the server from the host)

STEP4:
apply the ‘lsblk’ command to see the block devices

=>lsblk

There are two additional block devices name ‘sdb’ and ‘sdc’ er use this two drie to make a raid 0.

STEP5:
install the mdadm packge

=>yum update
=> yum install mdadm -y

STEP6:
check the version in the of the packages
=> mdadm –version

STEP7:
Examine the hard drive with mdadm

=> mdadm –examine /dev/sd[b-c]

STEP8:

Create partition for RAID

=>fdisk /dev/sdb

Follow below instructions for creating partitions.
1. Press ‘n‘ for creating new partition.
2. Then choose ‘P‘ for Primary partition.
3. Next select the partition number as 1.
4. Give the default value by just pressing two times Enter key.
5. Next press ‘P‘ to print the defined partition.

Follow below instructions for creating Linux raid auto on partitions.
1. Press ‘L‘ to list all available types.
2. Type ‘t‘to choose the partitions.
3. Choose ‘fd‘ for Linux raid auto and press Enter to apply.
4. Then again use ‘P‘ to print the changes what we have made.
5. Use ‘w‘ to write the changes.

[creating partition]

[creating raid on that paririon ]

[see the block devices]

STEP9:

Do the step 8 for the ‘sdc’

=>fdisk /dev/sdc

STEP10:

Examine with the ‘lsblk’

=>lsblk

STEP11:

Examine with the ‘mdadm’

STEP12:

Create RAID md Devices (with miror)

=>mdadm --create /dev/md0 --level=mirror --raid-devices=2 /dev/sd[b-c]1

STEP13:

See the Details of the RAID 0 devices

=>mdadm –detail /dev/md0

STEP14:

Assigning File partition on the File system

=>mkfs.ext4 /dev/md0

STEP15:

mount the volume

=>mkdir /mnt/raid0
=>mount /dev/md0 /mnt/raid0

STEP16:

check the mounted volume

=>df -h

STEP17:

check the block devices with lsblk

=>lsblk

STEP18:

Create a file inside the raid devices. To check that if one device is unplugged if the other have it.

STEP19:
unplug one device

STEP 20:
reboot the system and check the drive that is still connected and see if the backup is still there

Data is still there even one disk is unplugged